## Slide 1
计算机网络:自顶向下方法（第8版）第 8 版
吉姆·库罗斯，基思·罗斯·皮尔森，2020年
Chapter 5 Network Layer:
Control Plane
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on middleboxes (and Internet arch), Net neutrality, buffering …
lighter header font

## Slide 2: 网络层:“数据平面”路线图
网络层:概述
  数据面
  控制面
转发, SDN
  Match+action
  OpenFlow: match+action in action
中间件
路由器里面有什么
  输入端口，switch，输出端口
  缓冲区管理
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Notes: ，调度IP:互联网协议广义转发，简称SDN数据报的格式匹配操作+寻址OpenFlow: match+action in action网络地址转换造成IPv6网络层:4-3

## Slide 3: 广义转发:匹配加动作
1
2
0111
3
values in arriving
packet header
回顾:每台路由器包含一个转发表“匹配+动作”
抽象:匹配到达数据包中的位，采取动作
  广义转发:
  多个报头字段可以决定动作多种
  可能的动作:删除/复制/修改/日志报文
forwarding table
(aka: flow table)
(aka: flow table)
  基于目的转发:基于目的IP地址转发

## Slide 4: 流表抽象
流:由报头字段值定义(在链路、网络、传输层字段中)
广义转发:简单的报文处理规则
  匹配:报文报头字段中的模式值
  动作:对于匹配的报文:丢弃、转发、修改、匹配报文或将匹配的报文发送给控制器
  优先级:消除重叠模式的歧义
  计数器:#bytes和#packets
路由器的流表定义了路由器的匹配+动作规则
Flow table
match
action

## Slide 5: 流表抽象
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)
流:由报头字段值定义(在链路、网络、传输层字段中)
广义转发:简单的报文处理规则
  匹配:报文报头字段中的模式值
  动作:对于匹配的报文:丢弃、转发、修改、匹配报文或将匹配的报文发送给控制器
  优先级:消除重叠模式的歧义
  计数器:#bytes和#packets

## Slide 6: OpenFlow:流表项
Match
Action
Stats
将数据包转发到端口
删包
修改报头中的字段
封装并转发给控制器
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer

## Slide 7: OpenFlow: 例子
到达IP地址51.6.0.8的IP数据报应该被转发到路由器的输出端口6
阻断(不转发)所有发往TCP端口22 (ssh端口#)的数据报
阻断(不转发)主机128.119.1.1发送的所有数据报
Destination-based转发:
*
*
*
*
*
*
51.6.0.8
*
*
*
port6
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
*
*
防火墙：
drop
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
drop
*
128.119.1.1

## Slide 8: OpenFlow: examples
基于第二层目的的转发:
目的MAC地址为22:A7:23:11:E1:02的二层帧需要转发到输出端口3
*
*
*
*
*
*
*
*
*
port3
22:A7:23:
11:E1:02
*
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS

## Slide 9: OpenFlow抽象
Match +action:抽象统一了不同类型的设备
路由器
  match:最长目的IP前缀action:转发一个链接
开关
  match: 目标 MAC地址
  action:转发或批量
防火墙
  match: IP地址和TCP/UDP端口号
  action：允许或拒绝
NAT
  match: IP地址和端口action: 重写地址和端口

## Slide 10: OpenFlow例子
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
编排表可以创建网络范围的行为，例如:
来自主机h5和h6的数据报应该通过s1发送到h3或h4，然后从那里发送到s2

## Slide 11: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
编排表可以创建全网范围的行为，例如:
来自主机h5和h6的数据报应该通过s1发送到h3或h4，然后从那里发送到s2

## Slide 12: 广义转发:汇总
“匹配+动作”抽象:匹配任何层到达包头中的位，采取动作
在多个字段(链路层、网络层、传输层)上进行匹配
  本地动作:丢弃、转发、修改或发送匹配的报文到控制器
  “程序”网络范围内的行为
  “网络可编程性”的简单形式
  可编程的逐包“处理”
  历史根源:主动网络
  今天:更广义的编程:P4

## Slide 13: Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: 基于数据流的前向转发 (e.g., OpenFlow)
2. control, data plane separation
3. 控制面函数 external to data-plane switches
…
routing
access control
load
balance
4. 可编程控制应用

## Slide 14: Software defined networking (SDN)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
Data plane switches
快速, 简单, 商品化的 switches 实施一般化的数据面转发
data-plane forwarding (Section 4.4) in hardware
switch 数据流转发表由controller设置
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
与controller通信的协议 (e.g., OpenFlow)

## Slide 15: Software defined networking (SDN)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
SDN controller (network OS):
维护网络状态信息
与网络控制应用交互
via northbound API
与数据面交换机交互
via southbound API
分布式实施
for performance, scalability, fault-tolerance, robustness

## Slide 16: Software defined networking (SDN)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
network-control apps:
控制的大脑：
implement control functions using lower-level services, API provided by SND controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller

## Slide 17: Components of SDN controller
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
通讯层：
communication: communicate between SDN controller and controlled switches
网络状态管理层
network-wide state management : state of networks links, switches, services: a distributed database
接口层：
interface layer to network control apps: abstractions API

## Slide 18: OpenFlow协议
OpenFlow Controller
工作于controller, switch之间
使用TCP 交换消息
optional encryption
三种类型OpenFlow 消息:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc)

## Slide 19: OpenFlow: controller-to-switch 消息
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller

## Slide 20: OpenFlow: switch-to-controller 消息
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don’t “program” switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller

## Slide 21: SDN: 控制/数据平面交互实例
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Dijkstra’s link-state
routing
s1
s2
s3
s4
1
2
3
4
S1, 经历链路失效， OpenFlow 端口状态消息通知controller
1
SDN controller 接收OpenFlow 消息, 更新链路状态
2
Dijkstra’s 路由算法事先注册当链路失效时. 被调用.
3
Dijkstra’s 路由算法访问链路状态信息, 重新计算路由
4

## Slide 22: SDN: 控制/数据平面交互实例
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Dijkstra’s link-state
routing
s1
s2
s3
s4
5
6
1
2
3
4
SDN controller,链路状态路由应用与flow-table-computation 计算组件 重新计算flow tables
5
Controller 使用 OpenFlow 在switches 中更新flow tables
6

## Slide 23: OpenDaylight (ODL) controller
Network Orchestrations and Applications
Southbound API
Service Abstraction Layer (SAL)
config. and operational data store
REST/RESTCONF/NETCONF APIs
messaging
OpenFlow
NETCONF
SNMP
OVSDB
…
Northbound API
Traffic Engineering
…
Firewalling
Load Balancing
Basic Network Functions
Enhanced Services
…
…
Forwarding rules mgr.
AAA
Host
Tracker
Stats
mgr.
Switch
mgr.
Topology
processing
Service Abstraction Layer:
interconnects internal, external applications and services

## Slide 24: ONOS controller
Network Applications
Southbound API
Northbound API
Traffic Engineering
…
Firewalling
Load Balancing
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
REST API
Intent
ONOS
distributed core
statistics
devices
hosts
links
paths
flow rules
topology
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling

## Slide 25: SDN: 存在的问题
隐藏控制面:
dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: “baked in” from day one?
特定应用对网络协议的要求
  e.g., real-time, ultra-reliable, ultra-secure
可扩展性：Internet-scaling

## Slide 26: SDN与传统网络协议的未来
SDN计算与路由器-计算机转发表:
  这只是逻辑集中式计算与协议计算的一个例子
可以想象SDN计算的拥塞控制:
  控制器根据路由器(向控制器)报告的拥塞程度设置发送方速率
网络功能的实现(SDN与协议)将如何发展?

## Slide 27: 网络层:“控制平面”路线图
网络管理、配置
  SNMP
  NETCONF/YANG
概览
路由协议
  链路状态
  距离矢量
intra-ISP 路由: OSPF
ISP间路由: BGP
SDN 控制平面
Internet Control Message Protocol

## Slide 28: ICMP: 互联网控制报文协议
用于主机和路由器交换网络层信息
  错误报告:
  不可达主机, 网络, 端口, 协议
  echo request/reply (ping)
层次“above” IP:
  ICMP msgs 承载于IP数据报
ICMP message:
  错误类型,
  代码,
  引起错误IP数据报前8个字节
Type Code description
0 0 echo回答 (ping)
3 0 目的网络不可达
3 1 目的主机不可达
3 2 目的协议不可达
3 3 目的端口不可达
3 6 目的网络未知
3 7 目的主机未知
4 0 源抑制 (congestion
control - not used)
8 0 echo请求 (ping)
9 0 路由通告
10 0 路由发现
11 0 TTL 过期
12 0 IP 首部错误

## Slide 29: Traceroute and ICMP
3 probes
3 probes
3 probes
当 ICMP 消息回来后
source 计算 RTT
Traceroute 发送 3次
Stopping criterion
UDP 段最终到达主机
ICMP 返回
“host unreachable” 报文
(type 3, code 3)
源主机得到ICMP消息, 停止.
Source 发送不可达 UDP 端口号的报文至 dest
  第一个TTL =1
  第二个TTL=2, etc.
  不可端口号
  当 nth 数据报抵达 路由:
  路由丢弃数据报
  发送 source 一个 ICMP 消息 (type 11, code 0)
  消息包含路由名字& IP 地址

## Slide 30: 网络层:“控制平面”路线图
网络管理、配置
  SNMP
  NETCONF/YANG
概览
路由协议
  链路状态
  距离矢量
intra-ISP 路由: OSPF
ISP间路由: BGP
SDN 控制平面
Internet Control Message Protocol

## Slide 31: 什么是网络管理?
autonomous systems ( “network”): 1000个相互作用的硬件/软件组件
其他需要监控、组态、控制的复杂系统:
  喷气式飞机，核电站，还有其他?
"Network management 包括部署、集成以及硬件、软件和人的协调监控，测试，投票，配置，分析，评估，并控制网络和元素资源来满足实时性、操作性能和服务质量需求以合理的成本"

## Slide 32: 网络管理组成
managed device
managed device
managed device
managed device
managed device
agent
data
agent
data
agent
data
agent
data
agent
data
managing
server/controller
data
管理服务器: application, typically with network
managers (humans) in the loop
管理设备: equipment with manageable, configurable hardware, software components
数据:device “state” configuration data, operational data, device statistics
网络管理协议: used by managing server to query, configure, manage device; used by devices to inform managing server of data, events.

## Slide 33: 网络运营者的管理方法
managed device
managed device
managed device
managed device
managed device
agent
data
agent
data
agent
data
agent
data
agent
data
managing
server/controller
data
CLI (Command Line Interface)
  operator issues (types, scripts) direct to individual devices (e.g., vis ssh)
SNMP/MIB
  operator queries/sets devices data (MIB) using Simple Network Management Protocol (SNMP)
NETCONF/YANG
  more abstract, network-wide, holistic
  emphasis on multi-device configuration management.
  YANG: data modeling language
  NETCONF: communicate YANG-compatible actions/data to/from/among remote devices

## Slide 34: SNMP 协议
managed device
agent
data
managing
server/controller
data
request
response
trap message
传递MIB信息和命令的两种方式:
request/response mode
managed device
agent
data
managing
server/controller
data
trap mode

## Slide 35: SNMP协议: 信息类型
GetRequest
GetNextRequest
GetBulkRequest
manager-to-agent: “get me data”
(data instance, next data in list,
block of data).
信息类型
方法
SetRequest
manager-to-agent: set MIB value
Response
Agent-to-manager: value, response to Request
Trap
Agent-to-manager: inform manager
of exceptional event

## Slide 36: SNMP 协议: 消息格式
….
PDU
type
(0-3)
Request
ID
Error
Status
(0-5)
Error
Index
Name
Value
Name
Value
Get/set header
Variables to get/set
SNMP PDU
message types 0-3
….
PDU
type
4
Enterprise
Agent
Addr
Trap
Type
(0-7)
Specific
code
Time
stamp
Name
Value
Trap header
Trap info
message type 4

## Slide 37: SNMP: 管理信息库 (MIB)
管理设备的操作(和一些配置)数据
汇聚到设备MIB模块
  RFC中定义了400个MIB模块;更多特定于供应商的MIB
Object ID Name Type Comments
1.3.6.1.2.1.7.1 UDPInDatagrams 32-bit counter total # datagrams delivered
1.3.6.1.2.1.7.2 UDPNoPorts 32-bit counter # undeliverable datagrams (no application at port)
1.3.6.1.2.1.7.3 UDInErrors 32-bit counter # undeliverable datagrams (all other reasons)
1.3.6.1.2.1.7.4 UDPOutDatagrams 32-bit counter total # datagrams sent
1.3.6.1.2.1.7.5 udpTable SEQUENCE one entry for each port currently in use
agent
data
Structure of Management Information (SMI): 数据定义语言
UDP协议的MIB变量示例:

## Slide 38: NETCONF概述
目标: 主动管理/配置网络范围内的设备
在管理服务器和被管理网络设备之间进行操作
  操作:检索、设置、修改、激活配置
  跨多个设备的原子提交操作
  查询运行数据和统计信息
  订阅来自设备的通知
远程过程调用(RPC)范式
  用XML编码的NETCONF协议消息
  通过安全可靠的传输(如TLS)协议交换

## Slide 39: NETCONF初始化、交换、关闭
Session initiation,
capabilities exchange: <hello>
Session close: <close-session>
<rpc>
<rpc-reply>
<rpc>
<rpc-reply>
<rpc>
<rpc-reply>
<notification>
…
…
…
…
…
…
…
…
…
managing
server/controller
data
agent
data

## Slide 40: NETCONF操作选择
NETCONF 操作描述
<get-config> Retrieve all or part of a given configuration. A device may have multiple configurations.
<get> Retrieve all or part of both configuration state and operational state data.
<edit-config> Change specified (possibly running) configuration at managed device. Managed device <rpc-reply> contains <ok> or <rpcerror> with rollback.
<lock>, <unlock> Lock (unlock) configuration datastore at managed device (to lock out NETCONF, SNMP, or CLIs commands from other sources).
<create-subscription>, Enable event notification subscription from managed device
<notification>

## Slide 41: NETCONF RPC消息样例
note message id
change the running configuration
change MTU of Ethernet 0/0 interface to 1500
change a configuration

## Slide 42: YANG
数据建模语言用于指定NETCONF网络管理数据的结构、语法、语义
  内置数据类型，如SMI
XML文档描述设备，功能可以由YANG描述生成
能否表达数据之间的约束，这些约束必须由一个有效的NETCONF配置来满足
  确保NETCONF配置满足正确性、一致性约束
agent
data
managing
server/controller
data
NETCONF RPC message
<edit-config>
YANG-generated XML
</edit-config>
YANG
generated

## Slide 43: Network layer: “data plane” roadmap
Network layer: overview
What’s inside a router
IP: the Internet Protocol
Generalized Forwarding
中间件
  中间件的功能
  演变，互联网的架构原则

## Slide 44: Middleboxes
“在源主机和目的主机之间的数据路径上，除IP路由器的正常、标准功能外，执行其他功能的任何中间设备”
中间设备(RFC 3234)

## Slide 45: Middleboxes everywhere!
enterprise
network
national or global ISP
datacenter
network
NAT:家，蜂窝，机构
防火墙, IDS:公司、机构、服务提供商、互联网服务提供商
负载平衡器:企业、服务提供商、数据中心、移动网络
缓存:服务提供商、移动设备、cdn
特定应用:服务提供商，机构，CDN

## Slide 46: 中间件
最初:专有(封闭)硬件解决方案
向实现开放API的“白盒”硬件迈进
  远离专有硬件解决方案
  可编程的本地动作通过匹配+动作
  在软件领域走向创新/差异化
  SDN:(逻辑上)集中控制和配置管理，通常在私有/公共云中
  网络功能虚拟化(NFV):通过白盒网络、计算、存储提供可编程服务

## Slide 47: IP沙漏
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
互联网的“瘦腰”:
一个网络层协议:IP
必须在每一台(数十亿)联网设备上实现
物理层、链路层、传输层和应用层中的许多协议

## Slide 48: 中年时的IP沙漏
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
互联网中年“腰间赘肉”?中间层，在网络内部运行
NAT
NFV
Firewalls
caching

## Slide 49: 互联网的架构原则
“Internet社区的许多成员会争辩说，没有架构，只有传统，在最初的25年里没有写下来(或者至少不是IAB写下来的)。然而，总的来说，社区认为:
RFC 1958
目标是连接，工具是互联网协议，智能是端到端的，而不是隐藏在网络中。”
三个基本信念:
简单的连接性
IP协议:即智能窄腰
复杂性在网络边缘

## Slide 50: end-end参数
一些网络功能(例如，可靠的数据传输、拥塞)可以在网络中或在网络边缘实现
端到端实现可靠的数据传输
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
逐跳(网络内)实现可靠的数据传输

## Slide 51: The end-end 争论
“所讨论的功能只有在通信系统端点的应用程序的知识和帮助下才能完全正确地实现。因此，提供这种被质疑的功能作为通信系统本身的一个特征是不可能的。(有时，通信系统提供的功能的不完整版本可能有助于增强性能。
我们将这种针对低级函数实现的推理称为“端到端参数”。
Saltzer, Reed, Clark 1981
一些网络功能(例如，可靠的数据传输、拥塞)可以在网络中或在网络边缘实现

## Slide 52: 情报在哪里?
20th 世纪:
网络交换机的智能/计算
Internet (pre-2005)
智能，边缘计算
Internet (post-2005)
可编程网络设备智能、计算、边缘大规模应用级基础设施
Notes: The 20th century phone network had dumb network endpoints, really by definition. The end points were rotary phones that maybe only your parents and grandparents remember; they weren’t computers. They really were dumb devices, and therefore the phone network had programmable switches that were quite smart. All functionality – well, all of the intelligence - was implemented within the network. It HAD to be. The end systems could not do anything more than send digits and send audio signals.
When the Internet came along, the endpoints and the switches were both programmable computers. So where to put the complexity? RFC 1958 – the architectural principles of the Internet RFC - that says “intelligence is end to end rather than hidden in the network.” That puts the intelligence clearly at the edge, like we see here. And that’s possible because the edge devices are smart; they’re programmable. Well that’s the diagram as I remember it 20 years ago.
And in the 20 years since, as we see the rise of middleboxes and SDN, we’re now seeing intelligence (in software) layered on top of “dumb” whiteboxes within the network. So I might add a brain here today. And with datacenters and content distribution networks, we see even smarter and more sophisticated application-level infrastructure being connected at points within the network. So now there are clearly much much bigger, much more computationally intensive and complex, endpoints if you will in today’s Internet